## Slide 1: Unimproved Roads
Engineering Department
Date: October 2, 2023
City Commission Workshop

## Slide 2: Unimproved Roads
  Introduction:
  Current Special Assement District (SAD) Policy
  Selecting Water and Sewer Projects
    Scoring Process
    Priority Roads List
    Selecting Projects
  Unimproved to Improved Road Information
    Street Standard
    Lakeview Avenue
  Cost of Cape Seal and Improved Roads

## Slide 3
Current Special Assement District (SAD) Policy
  Sec 94 – Special Assement
    Revised in October 2021
  Initiation of Improvement by Commission
  Property owners may petition for an improvement

## Slide 4
SAD Unimproved Roads
  Cape Seal
    85% of the front-foot costs for improvement are assessed on all properties fronting on the improvement.
    25% of the side-foot costs for improvement are assessed on all residential properties siding on the improvement.
    85% of the side-foot costs for improvement are assessed on improved business properties siding on the improvement.
    25% of the side-foot costs for improvement are assessed on vacant business properties siding on the improvement.

## Slide 5
SAD Unimproved Roads
  Unimproved to Improved Road
    85% of the front-foot costs for improvement are assessed on all properties fronting on the improvement.
    For single family houses, if the longer side of a corner property faces the street being constructed, the City will pay two-thirds (2/3) of the cost of the assessment for that property. The property owner will be charged the remaining third (1/3). If the short side of a corner property faces the street to be constructed, the owner pays 100% of the assessment.

## Slide 6
Selecting Water and Sewer Projects
  Scoring Process
    Road: 0-100 points
    Sewer: 0-100 points
    Water: 0-100 points
    Higher points: Required Replacement
    Max Point: 300 points

## Slide 7
Road Scoring Process (up to 100 Points)
  PASER Rating
    In PASER:
      10: Great Condition of Pavement
      1: Poor Condition of Pavement
  Road Scoring Process (up to 100 Points):
    (10-2021 PASER Rating) x 10
    Example: PASER Rating 7
        (10 - 7) X 10 = 30
      Example: PASER Rating 2
    (10 - 2) X 10 = 80

## Slide 8
Water Scoring Process (up to 100 Points)
  Age (0-20)
    1 year old: 0 points
    75 years old (expected service life): 20 points
  Size (0-20)
    Current minimum size 8”
    6” water main: 10 points
    4” water main: 20 points
  Reinforcement (0-20)
    Water Pressures from water modeling:
    Points are assigned based on double the change in size recommended in the model
    Example: existing 6” water main, model calculates 12” water main: (6 x 2) = 12 points
  Frequency of Breaks (0-40)
    Each water main break equals 4 points
    City records go back to approximately 1960’s

## Slide 9
Sewer Scoring Process (up to 100 Points)
  Structural Condition (0-30)
    Segments with pipe fractures, cracks, and voids are scored higher
  Operation and Maintenance (0-20)
    Segments that require frequent cleanings due to slow flows, roots, etc. are scored higher
  Capacity Deficiency (0-40)
    Segments that are calculated as being too small for their service area
  Relief Sewer (0-10)
    Points are given to segments that help drain not only immediate area but upstream areas.

## Slide 10: Unimproved Road Scoring List

## Slide 11
Selecting Projects
  Input from City Departments:
    Fire Department
    Department of Public Service
  Utility Phasing
  Street Phasing

## Slide 12: Selecting Project Example

## Slide 13
Unimproved to Improved Road
Unimproved Road: Existing Width Varies

## Slide 14
Unimproved to Improved Road: Street Standard Width
Improved Road: 26’ wide standard width for Residential Street Width Policy
Note: Existing City streets that are measured less than 20 feet wide the City offers a 20 feet wide pavement with no parking on one side.

## Slide 15
Lakeview Ave.
Before
After

## Slide 16
Lakeview Ave.
Before
After

## Slide 17
Lakeview Ave.
Before
After

## Slide 18
Lakeview Ave.
Before
After

## Slide 19
Cost – Cape Seal
2022-2023 Cape Seal Program:
  SAD Estimated Cost: $38.00/lft
  SAD Projected Cost (from Bids and Construction): $27.00/lft +/-
  50’ Lot:
    Resident: $27.00*50’*85%= $1,147.50 (no payment option)
    City: $27.00*50’*15%= $202.50
2032-2033 Future Cape Seal:
  SAD Projected Cost (5% Inflation): $43.98/front +/-
  50’ Lot:
    Resident: $44.00*50’*85%= $1,870.00 (no payment option)
    City: $44.00*50’*15%= $330.00
Resident Cost 10 year Period: $3,017.50

## Slide 20
Cost – Improved Road
2022-2023 Improved Road:
  Estimated Cost for Paving Assement: $350.00/lft
  Estimate Cost for Drive Approach Assement: $11.75/sft
  50’ Lot:
    Resident: (($350.00*50’)+($11.75*130 sft))*85%= $16,173.38
    City: (($350.00*50’)+($11.75*130 sft))*15%= $2,854.13
Resident Cost: $16,173.38 (10 year payment option)

## Slide 21
Cost – Breakeven Point
 | Cape Seal | Improved Road
2023 | $1,147.50 | $16,173.38
2033 | $1,870.00 | 
2043 | $3,045.00 | 
2053 | $4,959.43 | 
2063 | $8,078.39 | 
 | $19,100.32 | $16,173.38